REPORT
*Descriptions of protocols are also given in the sender classes as comments*
Stop-and-Wait Protocol
 Description:
This protocol is used for sending single packet and blocking until receiving the acknowledgement for it from the receiver. The block is implemented with the msg value. If it is null, then the system is not blocked. The payload is given from the application layer. After confirming there are no packets being transmitted at the given time, the system becomes blocked until the packet is sent successfully. It is then wrapped into a package, with a sequence number, acknowledgement number and checksum attached. When ready, packet is sent to the receiver through the transport layer and a timer starts to count down. On the receiver side, the checksum value is extracted from the packet and recalculated by the same checksum generation algorithm to confirm the packet was sent without corruption. Then the packet is sent back with the corresponding acknowledgement. It is then checked if it matches the initial acknowledgement. In that case, the lock is released, timer is stopped, sequence number and acknowledgement number is increased in order to make the system ready for the next incoming message from the application, if there is one. If a packet is lost or corrupted while travelling to the receiver, since no packets will be sent back, a timeout will occur and the packet will be sent again. If a packet is lost or corrupted on its way back from the receiver to sender, the acknowledgement will be checked for confirmation, if it fails, a timeout will occur since the timer will not be stopped. Thus, the system only sends one packet and retries until it is certainly known to be transmitted correctly.

Go-Back-N Protocol
Description:
This protocol is used for sending N number of packets from a buffer. In this assignment N is 8. While sending the N size of window from the buffer, the system still accepts new payloads given from the application layer by wrapping them into new packets and adding them to the buffer. The buffer is an array of fixed sized to 50, instead of a cyclic buffer as in real-life scenarios. Once a message is received from the application layer while the base of the window is empty, it is directly sent through the network layer. If the packet is sent from the output method, the timer is set for one packet. If the packet is sent from the input method, the timer runs for the whole window whether the window is full or not, therefore, single packet time is multiplied with N is the interval for a timeout. In this case, the time for a single packet is set to 40, resulting to 40 * 8 = 320 for the whole window. On the receiver side, there is a single information, expected sequence number. This is to check if the packet received is the packet in order. If it is not, no further actions will be taken by the receiver. In the case it is, packet will be inspected to calculate and to compare checksum values in order to detect corruption. If the data is not corrupted, then a new packet is sent to the sender including the expected sequence number as acknowledgement value. Otherwise, no further action is taken by the receiver. Once the packet reaches the sender, the acknowledgement value is compared to base value whether if it is the latest unacknowledged packet in the window. If it is, then the base value is incremented. Then a final check exists to compare base value with sequence number to determine whether the end of window is reached. If it is the end of window, then the timer is stopped. If it isn't the end of buffer and if there are more packets in the window, then they are sent from the input method. In case a packet is lost or corrupted while travelling from the sender to receiver, then the receiver will not send anything which will cause for a timeout. If the packet is lost or corrupted on the way from the receiver to the sender, then it will fail the check on the sender side, leading to a timeout since the timer will not be stopped. The timeout is handled by resending all the packets in the window starting from the latest unacknowledged packet. Thus, as the system is fed payloads on a rate that the network layer can send, then the packets are sent instantly, otherwise they are added to the buffer to be sent in N sized windows when previous packets are acknowledged and control the failure of transmission by resending the window starting with the latest unacknowledged packet.